## Slide 1: IPM FOR Maintenance staff
Lesson 1 of 1
Self-Guided Education Module

## Slide 2: Learning Objectives
Explain the importance of routine, proactive building and facilities maintenance to maintain structural integrity and prevent pest entry and pest conducive conditions
Explain the importance of timely work order follow-up

## Slide 3: Learning Objectives
Describe the key elements of sanitation (clean environment) and exclusion, (habitat prevention) including: strategies, tactics, and tools
Describe the key elements of inspection and monitoring, including what to look for, where to look, tools used, and frequency
Explain the importance of effective communication, education, and cooperation between school staff

## Slide 4
What is IPM?
IPM = Integrated (Intelligent) Pest Management
A sensible, environmentally friendly, and effective way to solve pest problems
For more information on IPM, refer to resource sites https://www.epa.gov/managing-pests-schools &
                https://ipminstitute.org/projects/school-ipm-2020/updates/
                &
                http://ischoolpestmanager.org/

## Slide 5
Maintenance Staff and IPM
Maintenance responsibilities include everything from fixing furniture and drains, changing light bulbs and locks, installing appliances, collecting and emptying trash
Often they are asked to drop current tasks to attend to an emergency
Many are also responsible for the maintenance and care of landscaping and grounds surrounding a building
Please refer landscape/grounds module if you are responsible for landscape and/or grounds maintenance at your school

## Slide 6
Maintenance Staff and IPM
Maintenance staff are among the most important people in a school IPM program because they:
  are staff members who regularly see every part of the school and work with all other staff members
  perform a variety of tasks that are needed to maintain a healthy learning environment throughout the school
  regularly maintain the school to help keep pests out and therefore, reduce pest and pest management associated risks
Why should maintenance staff be involved in school IPM?

## Slide 7
Schools are great places for pests because there are many different areas and spaces they can thrive (e.g., food service, storage areas, classrooms, lockers, etc.)
Pests often find everything they need to survive: food, water and shelter, all in one place!
Pests Love To Go To School!

## Slide 8
Pests in schools
Being aware of common pests is the first step in their management - Problematic pests in and around schools include:
  Animal pests: Ants, cockroaches, flies, termites, scorpions, mosquitoes, rodents, pigeons, etc.
  Plant pests: Insects such as aphids, whiteflies, scales, and weeds

## Slide 9: 1.
IPM is Not an Additional Item on Your to-do List
Maintenance staff have very demanding jobs
IPM does not add to your responsibilities!
IPM only involves making slight changes in your daily activities, that will make your life easier and your working environment healthier!
IPM is not your job alone, it is everyone’s job
Maintenance staff with young helper, moving debris from fallen tree - Jason Moore, Street Superintendent, City of Beatrice, Nebraska

## Slide 10
Maintenance Staff and IPM
Dedicated maintenance staff actually implement IPM as they go about their regular daily duties
Rain gutters channel water away from building foundations, reduce erosion, prevent leaks in basements and crawlspaces, protect painted or stained surfaces by reducing exposure to water, and provide a means to collect rainwater for later use
Maintenance staff installing a rain gutter on a building - Ethoseo from Wikimedia commons

## Slide 11
Maintenance Staff and IPM
Routine, proactive maintenance is important
  To maintain structural integrity of the school buildings
  To prevent pest entry and pest conducive conditions
Gaps in foundation provide access to pests such as rodents - Dawn H. Gouge, University of Arizona

## Slide 12
Routine, Proactive Maintenance
Major factors that can affect structural integrity are moisture, wear and tear due to use, natural degradation, and pest activity
Minimize these effects by regularly monitoring your buildings
Perform structural repairs and reinforcements as soon as possible
Maintain structural integrity of buildings
Gaps in wall plaster can lead to moisture retention and weakening

## Slide 13
Routine, Proactive Maintenance
Moisture can cause structural weakening, unsightly discoloration and deformation, and support mold and other pests
Avoid moisture accumulation in and around the building, e.g., water puddling near foundation or walls
Waterproofing should be done using quality materials
Maintain structural integrity of buildings
Avoid water accumulation around building foundation – Shaku Nair, University of Arizona

## Slide 14
Routine, Proactive Maintenance
Incorrect placement of splash-guards (left) leads to puddling of water near building foundation and soil erosion. This has been corrected by correct placement of splash-guards (right) and addition of rocks and rip-rap to control erosion – Shaku Nair, University of Arizona
Maintain structural integrity of buildings

## Slide 15
Water leaks
Water leaks can indicate faulty plumbing, damaged roofs, or other problems
Water leaks can attract mold, carpenter ants, termites, flies, and rodents
They can also weaken the structure and lead to other problems such as electrical short circuits
Repair water leaks promptly – Dawn H. Gouge, University of Arizona
Routine, Proactive Maintenance
Drywall water damage
- Herbert Bernstein, WikiMedia Commons

## Slide 16
Routine, Proactive Maintenance
Be aware of structural pests attracted to water damaged wood such as termites, wood-destroying beetles, and mold
Monitor for pest activity and take necessary action as soon as they are noticed
Maintain structural integrity of buildings
Sign of western drywood termite damage - Kevin (ibkev2002), Flickr
Subterranean termite shelter tubes in a basement
- Larry Ralph Jr., Indiancrawlspacerepair

## Slide 17
Routine, Proactive Maintenance
Seal your buildings, make sure doors seal and self-close correctly
The vertical gap in the doorway (right) should be closed with brushes
Exterior doors should never be left propped open - Mice can enter through a ¼” gap
Effective door sweeps can cut pest complaints by 65%
Prevent pest entry
Even if this door is not propped open, the vertical gap gives easy entry to flying and crawling pests – Dawn H. Gouge, University of Arizona

## Slide 18
Routine, Proactive Maintenance
Check that escutcheon plates (pipe collars) are in place
Seal around pipe-chases and conduits that enter walls or drop ceilings
Loose escutcheon plates – Dawn H. Gouge, University of Arizona
Prevent pest entry
Gap in drop ceiling - Janet Hurley, Texas AgriLife Extension

## Slide 19
Routine, Proactive Maintenance
Sealing gaps
Use high quality silicon based (elastomeric) sealants to seal small cracks and crevices, and high quality concrete fillers, or steel wool to fill larger gaps
Sealing gaps around window frames keeps pests out and reduces heating/cooling expenses -WikiMedia Commons
Gaps in wall at pipe entry points Gaps have been sealed
- J. G. Kaufmann, WikiMedia Commons

## Slide 20
Routine, Proactive Maintenance
Seal around windows, doors, gaps in masonry, wall penetrations
Eliminate any unscreened access from outside
Ensure air doors are set correctly
Create space around your buildings - allow at least 1 foot gap between the building and vegetation
Prevent pest entry
Ensure that access panels are not left open – Jerry Jochim, Monroe County Community School Corporation
Ensure space between vegetation and building – Dawn H. Gouge, University of Arizona

## Slide 21
4.
Shrubs should be pruned away from buildings and shaped so they do not create places for rodents to hide
Keep tree limbs pruned at least six feet away from buildings
Remove vines climbing on buildings or growing low to the ground next to buildings to prevent pest access
Routine, Proactive Maintenance
These shrubs need trimming and pruning – Dawn H. Gouge, University of Arizona

## Slide 22
Routine, Proactive Maintenance
Grate and drain covers should be removed and cleaned out periodically – Dawn H. Gouge, University of Arizona
Avoid pest conducive conditions
Clean debris out of external drainage catch areas to reduce pest harborage
Prevent debris and moisture from accumulating near building walls and foundations
Pests such as rodents and flies are attracted to moist organic matter – Marc Lame, Indiana University

## Slide 23
Routine, Proactive Maintenance
Avoid pest conducive conditions
Pests such as cockroaches spend daytime hours harboring in cracks and crevices, including open plumbing and electrical pipe entry points, and unsealed crevices
Correct these conducive conditions, especially in areas where food is stored, prepared, or served
Sealing around escutcheon plates – Jerry Jochim, Monroe County Community School Corporation

## Slide 24
Remember that a pesticide applicator license may be required for pesticide applications on school property, including mold control, weed killers, insecticides, and rodent baits
Make certain that you are in compliance with local, state, and federal laws
Be aware of pesticides and chemicals that are legally allowed on school premises and ensure proper notifications are in place
When Using Pesticides
Routine, Proactive Maintenance

## Slide 25: Timely Work Order Follow-Up
Enforce timely responses to priority pest problems related to building repairs
Often a small fix can avoid a big problem
Repeated reporting of the same defect or damage is a waste of staff time
Whenever possible, centralize reports and track resolution times and costs
Use existing work-order systems when possible
Ensure doors close completely to keep pests out – Dawn H. Gouge, University of Arizona

## Slide 26
Sanitation and exclusion are basic steps in IPM
Sanitation involves cleaning, including the removal of hazardous wastes or materials that might pose health risks
In school environments, this involves proper disposal of garbage and other wastes, so that they do not interfere with school activities, or contaminate the school water supply or the school premises in general
Key Elements of Sanitation and Exclusion
Joseph Sohm, Shutterstock.com

## Slide 27
This dumpster is too close to the kitchen entryway
Good placement of dumpsters, in separate enclosed area, but lids should be closed
Waste management is an important part of sanitation
    Ensure that dumpsters are kept clean, covered, and well maintained
    Place dumpsters on a concrete or asphalt surface 20-30 feet away from building entryways
    Areas around the dumpster should be kept free of debris that can also shelter pests
Key Elements of Sanitation and Exclusion
Dawn H. Gouge, University of Arizona

## Slide 28: 1.
Your dumpster capacity should be sufficient; you should not have overflowing containers the day before collection
Discourage administrators from getting huge containers that are emptied only once a month
Dumpsters can become homes for feral cats, rats, and all kinds of pests
Poorly managed dumpsters and dumpster area – Marc Lame, Indiana University
Waste management
Key Elements of Sanitation and Exclusion
Notes: Objective 1

## Slide 29: 1.
Your service provider should rotate out dirty dumpsters for clean ones – you often need to request this
Dumpsters should be emptied at least weekly, more often in hot weather
Consider sealed, leak-proof, self-contained compactors, available in many sizes – Shaku Nair, University of Arizona
Waste management
Key Elements of Sanitation and Exclusion

## Slide 30
Sanitation also involves proper storage of supplies and materials - This helps to:
Prevent pest-conducive conditions
Permit proper cleaning and inspection
Key Elements of Sanitation and Exclusion
Cardboard covered wooden pallets are pest prone
- Dawn H. Gouge, University of Arizona
Aluminum dunnage racks are ideal, as you can see and clean beneath them

## Slide 31
Corrugations in cardboard boxes provide excellent harborage for cockroaches
Avoiding cardboard in storage is an important part of cockroach management
Pest Exclusion Strategies/Tactics
Kitchen pantry, before and after cardboard removal (inspect, date and organize supplies as they arrive) - Marc Lame, Indiana University

## Slide 32
Equipment cleaning
Keeping cleaning equipment in good and clean working condition is equally important to avoid attracting pests
Hang brooms 6 inches off the vertical wall
Food and other residues can accumulate in all of the following:
  Garbage receptacles
  Brooms, dusters, and brushes
  Mops and buckets
    Vacuum cleaners, polishers, scrubbers
Natural fiber brooms are difficult to clean, select cleaning tools that are easy to maintain

## Slide 33: Cleaning Equipment Maintenance and Storage
Emptying
Vacuum cleaners, floor scrubbers, and other pieces of equipment usually need to be emptied of debris or chemicals before they are stored
Wiping Down, Washing, and Rinsing
After use, each piece of equipment should be wiped down and, when appropriate, washed and rinsed to prevent build up of grit and grime

## Slide 34: Cleaning Equipment Maintenance and Storage
Storage
Once brooms, mops, and other tools are clean, store the items on off-the-floor racks, and away from the vertical wall
Clean and dry mop heads may be stored in transparent plastic totes or on wire shelving
Avoid heaping them on the floor or on solid shelving, they provide great harborage for spiders and cockroaches, and even nesting materials for mice
Store equipment off the floor and in a manner that will allow it to dry rapidly

## Slide 35: Thorough cleaning procedures
Above all, keep yourself safe, clean, and hygienic!
Remember to wash your hands thoroughly after cleaning up, especially if using chemicals products

## Slide 36: Pest exclusion involves denying pests access to food, water and shelter
Any sign of a pest should trigger a search for possible points of entry
Watch out for worn out door-sweeps and weather stripping
Watch out for hitchhikers in deliveries
  Check for signs of pest presence (droppings, pests, webbing or holes in boxes and insect monitoring traps in storage areas after a delivery)
Key Elements of Sanitation and Exclusion
This door needs new door-sweeps and weather stripping – Dawn H. Gouge, University of Arizona

## Slide 37
Replace worn door-sweeps - Effective sweeps drastically reduce the number of invading pests and can cut pest complaints by as much as 65% in some situations
Seal gaps, cracks, and crevices with suitable sealants
Cover windows and vents with wire mesh and replace with new wire mesh when broken
Pest Exclusion Strategies/Tactics
Torn wire mesh on a vent – Jerry Jochim, Monroe County Community School Corporation

## Slide 38
3.
P-traps in drains prevent gases, odors, and insects from entering buildings
Keep them filled with water, dry P-traps can create access to your building from the sewer for American cockroaches
Inspect drains periodically to prevent P-traps from drying out
Pest Exclusion Strategies/Tactics

## Slide 39
Avoid propping doors open, a propped door is both a security risk and a pest invitation
Close gaps that provide access to pests, young mice can squeeze through a gap the size of a dime; young rats need nickel-sized gaps; American cockroaches can pass through a gap the width of a quarter
Avoid clutter, both inside and outside, especially near external doorways
This space needs de-cluttering!
This door should be closed
Pest Exclusion Strategies/Tactics
Jerry Jochim, Monroe County Community School Corporation

## Slide 40: 2.
What to look for:
Pests
Signs of pests
Pest conducive conditions - pest opportunities inviting pests for food, water, and harborage
Key Elements of Inspection and Monitoring
Mouse poop on a spoon
The best way to know if or when pests are present is by regular inspection and monitoring
Cockroaches feeding on crumbs
Dawn H. Gouge, University of Arizona

## Slide 41: 2.
Where to look:
Dark corners
Hard-to-reach areas
Undisturbed places/under and behind stationary items
Warm and/or wet places
Food storage and/or preparation areas
Waste collection containers/areas
Suspended ceilings
Key Elements of Inspection and Monitoring
Regular, careful inspection helps to keep pests and pest-conducive conditions under control rapidly and efficiently – Dawn H. Gouge, University of Arizona

## Slide 42: 2.
Where to look:
Warm walls with penetrations
Compressor motor voids in equipment
Unsealed floors and floor to wall junctures
Undisturbed containers
Cardboard boxes
Clutter
Key Elements of Inspection and Monitoring
German cockroaches in telephone in heavily infested teachers lounge – Dawn H. Gouge, University of Arizona

## Slide 43
3.
Frequency: Along with daily duties, communicate in writing to IPM Coordinators and others about pest issues; document your actions
Record date, time, location and:
If actual pests have been spotted
Signs (evidence) of pests
Pest-conducive conditions
Key Elements of Inspection and Monitoring

## Slide 44: 2.
Tools:
Monitoring traps
Bright flashlight
Hand lens
Key Elements of Inspection and Monitoring
Turkestan cockroaches on monitoring trap in teachers lounge – Dawn H. Gouge, University of Arizona

## Slide 45
Maintenance Staff and IPM
Clean and well-maintained school premises are essential for the health and well-being of all people who learn, play or work in the area – Dawn H. Gouge, University of Arizona

## Slide 46
Effective Communication
Maintenance staff know more about the school premises than most other school staff - Let others know what you do, and how you can help them to manage pests
Get to know your lead front-line staff, contractors and other staff in your school
Communicate with them, show interest in their work, ask questions, help them to help you
Ricardo Zubiate teaching Salt Lake City School District Staff - Marc Lame, Indiana University

## Slide 47
Learn more about IPM from experts
Ask questions
Consider discussing IPM and its advantages with your colleagues and other school staff, faculty, and parents at PTA, staff and faculty meetings
Implementing IPM is easier with group support
Set an example; demonstrate your success with IPM
Effective Communication
Dr. Robert Corrigan, RMC Pest Management Consulting teaching - Mary Grisier, EPA Region 9

## Slide 48
“I am proud of
what I do to make my
school a better place
to learn and work”
Dan Vezie, Maricopa Unified School District, AZ
Maintenance Staff and IPM
Dan Vezie, Maricopa Unified School District receiving a recognition award – Shujuan Li, University of Arizona

## Slide 49: Check In!
In this lesson you learned:
The importance of routine, proactive maintenance to maintain structural integrity and prevent pest entry and pest conducive conditions
The importance of timely work order follow-up
Key elements of sanitation and exclusion, including: strategies, tactics and tools
Key elements of inspection and monitoring, including: what to look for, where to look, tools used and frequency
The importance of effective communication, education, and cooperation between school staff
  Congratulations, you have completed the School IPM for Maintenance Staff Module!

## Slide 50: Resources
Picture tour: IPM in Action – Safer Pest Control Project http://www.spcpweb.org/factsheets/IPM_Picture_Tour_w_cover.pdf
Get tough on pests in school facilities – NC State Cooperative Extension http://schoolipm.ncsu.edu/documents/Custodial_and_Maintenance_staff.pdf
School IPM for maintenance and grounds staff – IPM Institute http://schoolipm.ncsu.edu/documents/Custodial_and_Maintenance_staff.pdf
CA Dept. of Pesticide Regulation – IPM for Maintenance and Operations staff http://apps.cdpr.ca.gov/schoolipm/mo_staff/main.cfm
Implementing and IPM Program for Schools and Child care facilities – NC State University http://schoolipm.ncsu.edu/documents/Manual-Chapter2.pdf
Indoor and outdoor school IPM strategies http://www.extension.org/pages/20416/indoor-and-outdoor-school-ipm-strategies#.VNLCCy5kSpc